The passenger section of a jet airliner is in the shape of a cylindrical tube with a length of 35.0 m and an inner radius of 2.50 m. Its walls are lined with an insulating material 6.00 cm in thickness and having a thermal conductivity of 4.00 X 10-5 cal/s cm °C. A heater must maintain the interior temperature at 25.0°C while the outside temperature is              -35.0°C. What power must be supplied to the heater? (Use the result of Problem 70.)

SOLUTION

From problem 70, the rate of energy flow through the wall is

This is the rate of energy loss from the plane by heat, and consequently is the rate at which energy must be supplied in order to maintain a constant temperature.