In solar ponds constructed in Israel, the Sun’s energy is concentrated near the bottom of a salty pond. With the proper layering of salt in the water, convection is prevented, and temperatures of 100°C may be reached. Can you estimate the maximum efficiency with which useful energy can be extracted from the pond?

SOLUTION

Suppose the ambient temperature is 20°C. A gas can be heated to the temperature of the bottom of the pond, and allowed to cool as it blows through a turbine. The Carnot efficiency of such an engine is about