In practical heat engines, which are we better able to control: the temperature of the hot reservoir or the temperature of the cold reservoir? Explain.

SOLUTION

It is easier to control the temperature of a hot reservoir. If it cools down, then heat can be added through some external means, like an exothermic reaction. If it gets too hot, then heat can be allowed to “escape” into the atmosphere. To maintain the temperature of a cold reservoir, one must remove heat if the reservoir gets too hot. Doing this requires either an “even colder” reservoir, which you also must maintain, or an endothermic process.