In making raspberry jelly, 900 g of raspberry juice is combined with 930 g of sugar. The mixture starts at room temperature, 23.0°C, and is slowly heated on a stove until it reaches 220°F. It is then poured into heated jars and allowed to cool. Assume that the juice has the same specific heat as water. The specific heat of sucrose is 0.299 cal/g °C

Consider the heating process.

(a) Which of the following terms describe(s) this process: adiabatic, isobaric, isothermal, isovolumetric, cyclic, reversible, isentropic?

(b) How much energy does the mixture absorb?

(c) What is the minimum change in entropy of the jelly while it is heated?

SOLUTION

(a) 	The process is isobaric because it takes place under constant atmospheric pressure. As described by Newton’s third law, the stewing syrup must exert the same force on the air as the air exerts on it. The heating process is not adiabatic (energy goes in by heat), isothermal (T goes up), isovolumetic (it likely expands a bit), cyclic (it is different at the end), or isentropic (entropy increases). It could be made as nearly reversible as you wish, by not using a kitchen stove but a heater kept always just incrementally higher in temperature than the syrup. The process would then also be eternal, and impractical for food production.

(b) 	The final temperature is