A heat pump is to be installed in a region where the average outdoor temperature in the winter months is - 20°C. In view of this, why would it be advisable to place the outdoor compressor unit deep in the ground? Why are heat pumps not commonly used for heating in cold climates?

SOLUTION

Below the frost line, the winter temperature is much higher than the air or surface temperature. The earth is a huge reservoir of internal energy, but digging a lot of deep trenches is much more expensive than setting a heat-exchanger out on a concrete pad. A heat pump can have a much higher coefficient of performance when it is transferring energy by heat between reservoirs at close to the same temperature.